## Slide 1: CSC 3210 Computer Organization and Programming
Dr. Zulkar Nine
mnine@gsu.edu
Georgia State University
Spring 2021
Lab Work 2

## Slide 2: Lab Work 2 Instructions
Lab 2(a): Run a sample assembly language code (3 points)
Lab 2(b): Math problems (2 points)
Lab 2(c): Registers and Memory related Problems (5 points)
Due Date: 1/29/21 11:59 PM

## Slide 3: Lab 2(a)
Run a sample assembly code in Microsoft visual Studio

## Slide 4: Lab 2(a) Instructions
Follow the instructions to run the first program in assembly language.
Take screenshot/screenshots showing the code and the register contents.
Submit to the iCollege

## Slide 5: Create a new Project
Start Visual Studio
Click Create a new Project

## Slide 6: Create a new Project
Select C++ as language
Select Empty Project
Click Next

## Slide 7: Create a new Project
You can change the project
name as you like
Also you can change the
  project location
Click Next

## Slide 8: Create a new Project
Delete the
Following folders:
Header files
Resources Files, and
Source Files

## Slide 9: Create a new Project
To delete :
Select the folders
Right click on it
Select delete

## Slide 10: Create a new Project
Select Project Name on solution explorer
Right click on it
Go to Build Dependencies
Click on Build Customizations

## Slide 11: Create a new Project
Select mash(.target, .props)
Click ok

## Slide 12: Create a new Project
Right click on the Project name in the solution explorer
Click properties

## Slide 13: Create a new Project
Select Windows(/SUBSYSTEM:WINDOWS)
Click OK

## Slide 14: Create a new Project
Select Project name on solution explorer
Right click on it
Expand Add
Choose New Item

## Slide 15: Create a new Project
Select C++ File(.cpp)
Name: main.asm
Click Add

## Slide 16: Create a new Project
Select main.asm
Add your code
In the main.asm File.

## Slide 17: Sample Code
Type the sample code in the main.asm

## Slide 18: Run the code
Select Build Project (this will assemble and link your program) from the Build menu.
This will assemble and link your program

## Slide 19: Run the code
You should see messages like the following, indicating the build progress:
Note: if you see 1 failed or more, then there must be at least one error that needs to be corrected

## Slide 20: Run the code
Run the Program by selecting Start without Debugging from the Debug menu.
Press any keyto end running
- You will not see the result as the result is in a register
- See next slide

## Slide 21: Debug the code
Select Start Debugging from the Debug menu.

## Slide 22: Debug the code
You should see the register window in the bottom:

## Slide 23: Debug the code
  IF you don’t see the register window
  Go to
  Debug->Windows->Registers

## Slide 24: Debug the code
  The register window should appear during the debugging

## Slide 25: Debug the code
  To see the EFLAGs
  Right click on the register window and select “Flags”

## Slide 26: Debug the code
Select Step Over from the Debug menu.
  Depending on how Visual Studio was configured,
  Either the Fn+F10 function key or the Shift+F8 keys will execute the Step Over command.
  You can also use the button to stepover:
After you reach the “invoke ExistProcess,0”,
  Do not hit step over

## Slide 27: Debug the code
  After you reach the “invoke ExistProcess,0”
  Look at the eax register content and verify that its content is 11 (Which is B?).

## Slide 28: Debug the code
When you hit step over, the program will end, as there is nothing to execute after:
  “invoke ExistProcess,0”

## Slide 29: Debug the code
Another way to start a debugging session is
  set a breakpoint on a program statement by clicking the mouse in the vertical gray bar just to the left of the code window.
    A large red dot will mark the breakpoint location.
    Then you can run the program by selecting Start Debugging from the Debug menu.
If you try to set a breakpoint on a non-executable line, Visual Studio will just move the breakpoint forward to the next executable line when you run the program.

## Slide 30: Some Practice Problems
Don’t need to turn-in these problems

## Slide 31: Examples
What is the Most significant bit of the following binary number?
1000011010
Solution: 1

## Slide 32: Examples
What is the minimum number of binary bits to represent a decimal number 435644?
Solution:
Convert the decimal number to binary: 1101010010110111100
Count the number of bits: 19

## Slide 33: Examples
What is the minimum number of binary bits to represent the hexadecimal number 6A445?
Solution :
Convert the Hexadecimal number to binary:
0110 1010 0100 0100 0101
(2) Drop any leading zeros from the left side of the number:
110 1010 0100 0100 0101
(3) Count the number of bits: 19 bits

## Slide 34: Examples
What is the 8-bit binary representation of the following decimal number?
- 43
Solution:
Convert 43 into binary : 101011
Make the number 8-bit by adding 2 leading zeros: 0010 1011
Perform 2’s complement on 0010 1011
(3.1) Flip the bits: 1101 0100
(3.2) add 1 to it: 1101 0100 + 1 = 1101 0101

## Slide 35: Examples
Perform the following hexadecimal subtraction using 2’s complement.
A15F – 6ABC
Solution:
(1)Compute the 2’s complement of 6ABC:
(1.1) Reverse all the digits (subtract each digit from 15)
15 15 15 15
(-) 6 A B C
  9 5 4 3

## Slide 36: Examples
  (1.2) add 1 to it: 9543+1 = 9544
Add A15F + 9544
Carry:1 0 0 1
A 1 5 F
9 5 4 4
3 6 A 3
Ignore the last carry.

## Slide 37: Examples
What is the decimal representation of following signed numbers?
10110111
Solution: MSB is 1, so the number is negative
Perform a 2’s complement: 1011 0111
(1.1) flip the bits : 0100 1000
(1.2) add 2 to it: 0100 1000 + 1 = 0100 1001
(2) Convert the number into decimal: 73
(3) Sign bit was 1, so the number is -73

## Slide 38: Examples
How many selector bits required for a four input multiplexer?
Solution:
A multiplexer uses selector bits to select specific input and let that input available to the output.
When a multiplexer has two inputs, it can enumerate the inputs as 0 and 1.
When a multiplexer has 4 inputs, it needs two bits to enumerate them.
Selector bits - 00 – input 1
01 – input 2
10 – input 3
11 – input 4

## Slide 39: Lab 2(b)
Submit these Math Problems to iCollege

## Slide 40: Lab 2(b) : Submission
Solve the Problems provided in slide 41 to 42.
You can do your work in a text editor (Microsoft word, open office, etc.)
Or you can do it in a piece of paper, then scan or take a picture of the paper.
Convert them into pdf and submit in the icollege.

## Slide 41: Lab 2(b) Problem 1
Design a 8-bit full adder. Draw the block diagram. [Hint: Lecture]

## Slide 42: Lab 2(b) Problem 2
Draw the circuit for the following Boolean expression:
P = (X and Y) or (not X or Z) [Hint: Lecture]

## Slide 43: Registers and Memory
A review

## Slide 44: Registers
Registers are storage locations inside the processor.
A register can be accessed more quickly than a memory location (Why?).
Different registers serve different purposes.
Some of them are described below:
1
2
4
3

## Slide 45: General-Purpose Registers (8 registers)
There are eight general purpose registers
  EAX –
    All major calculations take place in EAX,
    making it similar to a dedicated accumulator register.
  EDX –
    The data register is the an extension to the accumulator.
    It is most useful for storing data related to the accumulator's current calculation.

## Slide 46: General-Purpose Registers
There are eight general purpose registers
  ECX –
    Like the variable i in high-level languages, the count register is the universal loop counter.
  EBX –
    In 16-bit mode, the base register was useful as a pointer.
    Now, it is completely free for extra storage space.

## Slide 47: General-Purpose Registers
There are eight general purpose registers
  ESP –
    ESP is the sacred stack pointer.
    With the important PUSH, POP, CALL, and RET instructions requiring it's value,
      there is never a good reason to use the stack pointer for anything else.
  EBP –
    In functions that store parameters or variables on the stack,
      the base pointer holds the location of the current stack frame.
    In other situations, however, EBP is a free data-storage register.

## Slide 48: General-Purpose Registers
There are eight general purpose registers
  EDI –
    Every loop must store its result somewhere,
    and the destination index points to that place.
  ESI –
    In loops that process data,
    the source index holds the location of the input data stream.

## Slide 49: General-Purpose Registers
Accessing Parts of Registers

## Slide 50: General-Purpose Registers
Bits are stored in any registers right to left
  Ex: 32-bit Register (referring to bits storage not bytes)
Right
Left

## Slide 51: General-Purpose Registers
Bytes are stored right to left too
Byte4 | Byte3 | Byte2 | Byte1
0
31
A2B1C3D4h
Byte1
Byte2
Byte3
Byte4

## Slide 52: Segment Registers
There are six segment registers
CS – code segment: hold program instructions
DS – data segment: hold variables
SS – stack segment: holds local function variables and function parameters.
ES, FS, GS - additional segments: can be used in a similar way as the other segment registers.

## Slide 53: Instruction Pointer Register
EIP – instruction pointer (also called program counter):
  contains the address of the next instruction to be executed .
It is also known as PC (Program Counter)

## Slide 54: EFLAGS Register
  EFLAGS- a register consists of individual binary bits that
  control the operation of the CPU or
  reflect the outcome of some CPU operation.
Thus, we have status and control flags
  Each flag is a single binary bit

## Slide 55: EFLAGS Register
Carry
  unsigned arithmetic out of range
Overflow
  signed arithmetic out of range
Sign
  result is negative
Zero
  result is zero
Status flags record certain information about the most recent arithmetic or logical operation.
A flag is set when it equals 1;
it is clear (or reset) when it equals 0.
Note: Control flags are out of the scope of this class

## Slide 56: Some Practice Examples
Don’t need to turn-in these problems

## Slide 57: Practice Problems
1. Which flag is set when the result of an unsigned arithmetic operation is too large to fit into the destination?
2. Which flag is set when the result of a signed arithmetic operation is either too large or too small to fit into the destination?
3. Which flag is set when an arithmetic or logical operation generates a negative result?

## Slide 58: Practice Examples
4. Show the EDX register and the size and position of the DH, DL, and DX within it.

## Slide 59: Lab 2(c)
Submit these Problems

## Slide 60: Lab 2(c) : Submission
Solve the Problems provided in slide 61 to 62.
You can do your work in a text editor (Microsoft word, open office, etc.)
Or you can do it in a piece of paper, then scan or take a picture of the paper.
Convert them into pdf and submit in the iCollege.

## Slide 61: Lab 2(c) Problems
2. Store the following value in EAX register: 12784569h
0
31
4 bytes

## Slide 62: Lab 2(c) Problems
6. For each add instruction in this exercise, assume that EAX contains the given contents before the instruction is executed.
Give the contents of EAX as well as the values of the CF, OF, SF, ZF after the instruction is executed.
All numbers are in hex. (Hint: add eax, 40 will add 40 to the contents of register eax and stores the result back in eax)
Contents of EAX (Before) | Instruction | Contents of EAX (After) | CF | OF | SF | ZF
00000040 | add eax, 40 |  |  |  |  | 
FFFFFF40 | add eax, 40 |  |  |  |  | 
00000040 | add eax, -40 |  |  |  |  | 
Assume that numbers are signed integers